## Slide 1
Hotel Network Infrastructure Design
Course: CIE 447 – Computer Networks
Semester: Spring 2025 Instructor: Dr Mohamed Samir Eng: Mohamed Saleh Eng Amira EzzEldein

## Slide 2
Project Overview
Network Scope
3-floor hotel, scalable design
Subnetting
Address block 192.168.2.0/24 with VLANs
Routing Protocol
OSPF for inter-floor routing
Services
DHCP, DNS, Web servers deployed

## Slide 3
Network Topology
Floors & Devices
3 Floors, separate routers
Layer 2 switches connecting departments
Router Placement
All routers centralized on 3rd floor IT room
Connections
Serial DCE cables link routers
VLANs
Consistent VLANs deployed across floors

## Slide 4
Subnetting Strategy
Department
Subnet Mask
VLAN
IP Range
Reception
/27
80
192.168.2.64–95
Store
/29
70
192.168.2.120–127
Logistics
/29
60
192.168.2.136–143
Finance
/28
50
192.168.2.96–111
HR
/28
40
192.168.2.128–143
Sales
/27
30
192.168.2.32–63
Admin
/27
20
192.168.2.160–182
IT
/26
10
192.168.2.0–63

## Slide 5
VLAN and Server Assignments
DNS Server
VLAN 20, IP 192.168.2.114
Web Server
VLAN 50, IP 192.168.2.98
DHCP Servers
VLAN 80 – 192.168.2.66
VLAN 40 – 192.168.2.130
VLAN 10 – 192.168.2.2

## Slide 6
Routing Configuration
Routing Protocol
OSPF between routers for dynamic routing
Router IDs
Loopback interfaces assigned uniquely
Router-on-a-Stick
Subinterfaces manage VLAN routing
Serial Link IPs
R1-R2: 192.168.2.148/30
R2-R3: 192.168.2.152/30
R1-R3: 192.168.2.156/30

## Slide 7
DHCP Pool Configuration
1
DHCP Setup
Subnet, gateway, DNS assigned per pool
2
Conflict Resolution
Admin VLAN subnet size adjusted to /28
3
Overlap Handling
Eliminated overlapping IP ranges
4
Testing
Dynamic client lease verification performed

## Slide 8
Relocation Scenario
Sales Department
Moved to headquarters with extended link connection
Admin Department
Moved to first floor, VLAN 20 reassigned
Config Migration
VLAN and DHCP pool shifted to floor 1 router

## Slide 9
Implementation Steps for Relocation
Remove Old Config
Delete VLAN 20 subinterface on floor 3 router
Apply New Config
Add VLAN 20 on floor 1 router and DHCP server
Switch Port Updates
Reassign physical switch ports for Admin
Verification
Test connectivity and web access after changes

## Slide 10
Testing and Verification
Connectivity
Ping tests passed between all departments
Website Access
Accessible: www.hotelservices.com
DNS Functionality
Resolves correctly for all clients
Routing
OSPF routes verified via show commands
DHCP
Leases correctly assigned to clients

## Slide 11
Conclusion
Successfully designed a modular, scalable hotel network
Efficient use of subnets and VLANs
Dynamic routing with OSPF
DHCP and DNS functioning as expected
Network adapted seamlessly to relocation scenario